JSG21-10KM/JSG23-12KM

Introduction:

Name: Gas Instantaneous Water Heater for Household use

Types: JSG21-10KM/JSG23-12KM

Feature and benefits:

1. Balance type gas water heater is with intelligent subsection combustion technology and AI memory system.

2. Low start-up water pressure and wide-range water temperature adjustment from 35℃～65℃.

3. It is with low energy consumption and high heat efficiency which can reach 90%.

4. It has LCD display touch monitor, multiple safety system and automatic fault detecting code.

Advantages:

1.  Balance type gas water heater has AI constant temperature engine.

- DC electrodeless frequency conversion combustion technology.

- Precise magnetic levitation type gas proportional valve.

- Z-type combustor with stable flame core.

- Forced combustion technology with full seal.

- Water flow sensor with high precision.

- Oxygen-free copper water bank with high efficiency and environment friendly.

- All products are with CE certificate.

Specification

| Type | JSG21-10KM | JSG23-12KM |
| --- | --- | --- |
| Rated heat load（kW) | 21 | 23 |
| Rated capability of hot water supply (△T=25℃） | 10kg/min | 12kg/min |
| Rated gas pressure | Liquefied petroleum gas 2800 pa |
|  | Natural gas 2000 pa |
|  | Manufactured gas 1000 pa |
| Control method | By outlet valve |
| Exhaust method | Forced type |
| Applicable water pressure (Mpa) | 0.02~1.0 |
| Gas entrance | G1/2 or G3/4 |
| Cold water inlet | G1/2 |
| Hot water outlet | G1/2 |
| Product size（mm) | Ф60 and Ф100 | Ф60 and Ф100 |
| Control method | 567×350×134 | 567×350×134 |
| Package size（mm) | 755×435×235 | 755×435×235 |
| Gross weight/net weight（kg） | 15.9/14.5 | 15.9/14.5 |
| Container number 20'/40'/40'HQ | 290/595/670 | 290/595/670 |